NOTIFICATION

The following notification is being circulated in accordance with Article 10.6

| 1. | Notifying Member: Turkey If applicable, name of local government involved (Article 3.2 and 7.2): |
| --- | --- |
| 2. | Agency responsible: Ministry of Industry and Technology DG for EU and Foreign Affairs Mustafa Kemal Mah. Dumlupinar Bulvari Eskişehir Yolu 2151. Cad. No:154 Cankaya - Ankara/ Turkey Tel: +90 (312) 201 60 82 Fax: +90 (312) 219 68 64 E-mail:sumeyye.sabanci@sanayi.gov.tr Name and address (including telephone and fax numbers, email and website addresses, if available) of agency or authority designated to handle comments regarding the notification shall be indicated if different from above: Turkey-TBT Enquiry Point Ministry of Trade DG of Product Safety and Inspection Sogutozu Mah. 2180. Sk. No:63 06530 Çankaya-Ankara / Turkey Tel: +90 (312) 204 89 37 / 89 52 Fax: +90 (312) 212 87 68 E-mail: tbt@ticaret.gov.tr |
| 3. | Notified under Article 2.9.2 [X], 2.10.1 [ ], 5.6.2 [ ], 5.7.1 [ ], other: |
| 4. | Products covered (HS or CCCN where applicable, otherwise national tariff heading. ICS numbers may be provided in addition, where applicable): Electric motors and variable speed drives |
| 5. | Title, number of pages and language(s) of the notified document: Draft Communique on Ecodesign Requirements for Electric Motors and Variable Speed Drives (SGM:2021/16) (2019/1781/EU) (25 page(s), in English) |
| 6. | Description of content: (1) This Communique applies to the following products: a) induction electric motors without brushes, commutators, slip rings or electrical connections to the rotor, rated for operation on a 50 Hz, 60 Hz or 50/60 Hz sinusoidal voltage, that: 1) have two, four, six or eight poles; 2) have a rated voltage UN above 50 V and up to and including 1 000 V; 3) have a rated power output PN from 0,12 kW up to and including 1 000 kW; 4) are rated on the basis of continuous duty operation; and 5) are rated for direct on-line operation; b) variable speed drives with 3 phases input that: 1) are rated for operating with one motor referred to in point 1(a) of this article, within the 0,12 kW-1 000 kW motor rated output range; 2) have a rated voltage above 100 V and up to and including 1 000 V AC; 3) have only one AC voltage output. (2) The requirements in section 1, and points (a), (b), (d), (e), (f), (g), (ğ), (h), (1) section 2, and (13) of section 3 (a) of Annex I shall not apply to the following motors: a) motors completely integrated into a product (for example into a gear, pump, fan or compressor) and whose energy performance cannot be tested independently from the product, even with the provision of a temporary end-shield and drive-end bearing; the motor must share common components (apart from connectors such as bolts) with the driven unit (for example, a shaft or housing) and shall not be designed in such a way that the motor can be separated in its entirety from the driven unit and operate independently. The process of separation shall have the consequence of rendering the motor inoperative; b) motors with an integrated variable speed drive (compact drives) whose energy performance cannot be tested independently from the variable speed drive; c) motors with an integrated brake which forms an integral part of the inner motor construction and can neither be removed nor powered by a separate power source during the testing of the motor efficiency; ç) motors specifically designed and specified to operate exclusively: 1) at altitudes exceeding 4 000 metres above sea-level; 2) where ambient air temperatures exceed 60°C; 3) in maximum operating temperature above 400°C; 4) where ambient air temperatures are less than 30°C; or 5) where the water coolant temperature at the inlet to a product is below 0°C or above 32°C; d) motors specifically designed and specified to operate wholly immersed in a liquid; e) motors specifically qualified for the safety of nuclear installations, f) explosion-protected motors specifically designed and certified for mining, as defined in section 1 of Annex I of Regulation on the Equipment and Protective Systems Intended for Use In Potentially Explosive Atmospheres (2014/34/EU) published in the Official Gazette dated 30/06/2016 and numbered 29758. g) motors in cordless or battery-operated equipment; ğ) motors in hand-held equipment whose weight is supported by hand during operation; h) motors in hand-guided mobile equipment moved while in operation; 1) motors with mechanical commutators; i) Totally Enclosed Non-Ventilated (TENV) motors; j) motors placed on the market before 1 July 2029 as substitutes for identical motors integrated in products placed on the market before 1 July 2021 for motors referred to in Annex I. Part 1 (1)(a) and before 1 July 2023 for motors referred to in Annex I. Part 1 (1)(b) , and specifically marketed as such; k) multi-speed motors, i.e. motors with multiple windings or with a switchable winding, providing a different number of poles and speeds; l) motors designed specifically for the traction of electric vehicles. (3) The requirements in section 3, and points (1), (2), (5), (6), (7), (8), (9) and (10) of section 4 and section 3 of Annex I shall not apply to the following VSDs: a) VSDs integrated into a product and whose energy performance cannot be tested independently from the product, that is to say that an attempt to do so would render the VSD or the product inoperative; b) VSDs qualified specifically for the safety of nuclear installations defined in Directive on Nuclear Safety Controls and Sanctions published in the Official Gazette dated 13/10/2007 and numbered 26642, c) regenerative drives; ç) drives with sinusoidal input current. d) VSDs consisting of a single cabinet, comprising VSDs which are all in conformity with this Communique. |
| 7. | Objective and rationale, including the nature of urgent problems where applicable: The purpose of this Communique is to establish ecodesign requirements for the placing on the market or the putting into service of electric motors and variable speed drives, including where they are integrated in other products, related to the implementation of the Regulation on the Ecodesign of Energy-Related Products which was put into effect with the Cabinet Decree dated 23/6/2010 and numbered 2010/643; Protection of the environment; Harmonization |
| 8. | Relevant documents: This Communique has been prepared based on Commission Regulation No 2019/1781/EU laying down ecodesign requirements for electric motors and variable speed drives pursuant to Directive 2009/125/EC of the European Parliament and of the Council, repealing Commission Regulation (EC) No 640/2009 in the framework of alignment with the European Union legislation. This Communique has been prepared on the basis of the Law No. 4703 of 29/6/2001 on the Preparation and Implementation of Technical Legislation on Products and Presidential Decree No. 1 on the Presidency Organization published in the Official Gazette No. 30474 dated 10/7/2018. |
| 9. | Proposed date of adoption: The regulation will be adopted upon its publication. Proposed date of entry into force: Paragraph 1 of Article 9 of this Communique shall enter into force on the date of its publication and other provisions shall enter into force on 01/07/2021. |
| 10. | Final date for comments: 14 April 2021; The relevant legislation will be put into effect within the scope of harmonization with the EU legislation. |
| 11. | Texts available from: National enquiry point [X] or address, telephone and fax numbers and email and website addresses, if available, of other body: Ministry of Industry and Technology DG for EU and Foreign Affairs Mustafa Kemal Mah. Dumlupinar Bulvari Eskişehir Yolu 2151. Cad. No:154 Cankaya - Ankara/ Turkey Tel: +90 (312) 201 60 82 Fax: +90 (312) 219 68 64 E-mail: sumeyye.sabanci@sanayi.gov.tr https://members.wto.org/crnattachments/2021/TBT/TUR/21_2541_00_e.pdf |